## Slide 1
Examples of commonly used terms for water management data and suggested controlled vocabulary (to become a community standard)
A Proposed Water Management Data Model (WaM-DaM)
Adel M. Abdallah & David E. Rosenberg
Utah Water Research Laboratory, Utah State University, Logan – Utah
2013 CUAHSI Conference on Hydroinformatics and Modeling, July 19-21, 2013
EPSCoR
EPS 1135482
We are proposing the Water Management Data Model (WaM-DaM) to organize, share, and publish water management data. WaM-DaM provides a set of specifications for a generic, open-source data management system to support water management and hydrologic modeling. WaM-DaM helps to automatically transfer water management data across many models and platforms. The data model is being developed as part of a multi-institutional research project called “Cyber-Infrastructure to Advance High Performance Water Resource Modeling” (CI-Water). First, we reconstructed the data models of several common models like WEAP, HEC-ResSim and HydroPlatform to understand the heterogeneity of water management data. Then we listed vocabularies used to describe water management data. We reviewed the ODM capabilities to represent time series data and metadata to incorporate it in our model. Finally, we formulated the conceptual design of the WaM-DaM using relational database concepts.
We use data objects to spatially and temporary represent water management data and infrastructure. Object types like nodes and links spatially represent the network of water management system components including infrastructure like reservoirs and canals, water demands, and operations of infrastructure to satisfy demands. The WaM-DaM organizes input and output data to several common models like WEAP and HEC-ResSim. Queries against the WaM-DaM allow the user to automatically transfer data with specific formats, scales, and semantics as required by the WEAP or HEC-ResSim models. At the same time, the WaM-DaM is flexible and can support other models by allowing more objects to be defined, subsequently populated, and queried.
We seek feedback from the research community on the representation of the data model, lists of controlled vocabulary, and WaM-DaM capabilities to support community needs. Finally, we intend to publish and register the WaM-DaM with CUAHSI-HIS through HydroServer to facilitate the searching, discovery, and pre-processing of data through HydroDesktop like in the Observations Data Model (ODM).
Abstract
Your Feedback?
We seek your feedback on the WaM-DaM. Particularly:
What hydrologic and water management software/models do you use?
How do these models partition space (e.g., nodes, links, triangles, grids, etc.)?
What data types do the models require (e.g., time series, table, parameter, other?)
Will the proposed WaM-DaM capabilities of organizing, sharing, and publishing water management data support your modeling needs?
Other suggestions/feedback?
WaM-DaM Functionality and Conceptual Design
Example water management data for natural and engineered system components that we wish to support:
Water Management Data
System Component | Physical Attributes | Operational Attributes | Example Model Output
Rivers | Length, connectivity, inflow, reach gain/losses | Minimum required flows | Flow and quality
Reservoirs | Capacity, release structures, elevation-storage-area curves | Purposes, zones, release rules, delivery targets | Releases, water level, storage volume
Canals | Length, connectivity, flow capacity | Diversion rules, demands served | Flow rate
Hydropower | Turbine type, capacity, efficiency | Energy demands | Energy generated
Demand site | Water use(s) | Priority, timing, water required | Deliveries, shortages
Groundwater | Recharge, well locations | Pump capacities, artificial recharge | Depth to groundwater, withdraw rates
Finalize a draft of the WaM-DaM schema and seek feedback from the CI-Water teams and interested researchers
Implement a physical model of the WaM-DaM schema
Collaborate with HydroPlatform developers to implement and interface the WaM-DaM for HydroPlatform 2.0
Write codes for tools to query and serve water management data to desired models like WEAP and HEC-ResSim by automatically transfer their data back and forth to WaM-DaM
Ultimately, we intend to publish and register the WaM-DaM with CUAHSI-HIS to facilitate the searching, discovery, and pre-processing of data like HydroDesktop with the ODM
Future Work
Need consistent, descriptive, and integrated data model to organize, prepare, and publish water management data and support modeling
Discover and share data among nearly 30 agencies
Automatically transfer water management data across models and platforms like:
Motivations
Reversed engineer the data models of several water management models like WEAP and HEC-ResSim to understand the heterogeneity of water management data
Reconstructed the data model of HydroPlatform which is an open-source software platform for water resource management models. The software manages and displays information about water resource systems
Reviewed the Observations Data model (ODM) and study its capabilities in supporting time series data and metadata
Listed vocabularies that are commonly used to describe water management data
Used the relational database concepts to represent water management objects and their connectivity
Methods
The conceptual design of the WaM-DaM is shown in Fig. 2 and is briefly described here:
First, the user defines a project, then a water management network within the project. The user also can define scenarios for networks
Second, the user uses a customizable data objects that allow adding descriptive attributes to each object. Objects can be nodes (e.g., reservoirs) or links (e.g., rivers). Each object attribute have a data type like (parameter, time series, and table). The WaM-DaM introduces controlled vocabulary to enforce the use of consistent object and attribute terms
Third, the user creates instances of these objects and defines connectivity among them. Each link has a start and end node
Finally, the user populates the values of network’s objects attributes with water management data and its associated metadata
Controlled Vocabulary
Suggested controlled vocabulary | Commonly used terms by models
Reservoir | Reservoir, dam, storage reservoir, lake area
Zone | Zone, pool
Hydropower | Energy, power, power plant, run of the river hydro
Node | Junction, node, station, stream station, site, stream flow gauge
Maximum hydraulic capacity | Maximum hydraulic capacity, maximum capacity
Evaporation | Evap., evaporation
Link | Channel, fork, link, element, branch, tributary, creek, reach
River Basin | Basin, watershed, river basin, catchment, watershed
Demand site | Demand site, service area, water use location, diversion, consumptive use, flow requirement, diversion outflow consumption
Storage | Storage, volume
Supply | Supply, import, return flow, resource
When implemented, WaM-DaM will perform the following tasks as shown in Fig. 1:
read/ingest water management data from files created by stakeholders, existing models output, and online published data,
store data in a common, structured, and self-describing format,
retrieve stored data and transform it to the specific format needed to run a water management model like WEAP, HEC-ResSim, or others
transfer existing model outputs to the WaM-DaM and then serve it as input data to other models
WaM-DaM Functionality
WaM-DaM Conceptual Design
Fig. 1
Fig. 2
Notes: Format and print size is 36*56 inches. Can print it at the ENGR lab
This size fits easily on the board size of 4*8 ft (48*96 inch)